2️⃣ Problem with Slow Software Microcontrollers
If a fast master (hardware I²C) starts transmitting on the bus:
- A slow software MCU may miss the beginning of communication because it checks the bus at a lower rate.
- If the start condition is very short, the software MCU might not detect it immediately.
Solution: Use a special “long start” procedure to give slower devices time to detect bus activity.

3️⃣ The “Long Start Procedure”
This is what the manual is describing:
1. START condition (S)
  1. Standard I²C start (SDA goes LOW while SCL HIGH)
2. START byte (0000 0001)
  1. A special byte sent immediately after START
  2. Purpose: allow slow MCUs to sample SDA line at low rate
  3. The seven zeros are easily detected as LOW levels.
3. Acknowledge clock pulse (ACK)
  1. Part of standard byte handling, but no device actually acknowledges this START byte.
  2. It’s just to keep the bus format correct.
4. Repeated START (Sr)
  1. After detecting the START byte, all devices resynchronize using this repeated START.
  2. Hardware receivers ignore the START byte and reset at repeated START.

4️⃣ How the Slow MCU Uses This
- MCU samples SDA slowly at first.
- Once it sees one of the zeros in the START byte (SDA LOW), it switches to higher sampling rate.
- Now it can detect the repeated START (Sr) accurately.
- After Sr, communication proceeds normally.
Essentially: the START byte is a “wake-up signal” for slower devices.

5️⃣ Why This Works
- Fast devices ignore the START byte; they just proceed.
- Slow devices get extra time to detect the bus activity.
- No data corruption occurs.
- ACK is included only to conform to byte structure, but no one actually responds.